General Info:
VHDL is not case sensitive, this includes key words as well as user defined variables. General convention is to leave key words lower case and use upper case for user defined variables. Loosely followed.

In system verilog this <= signals we are using sequential logic or a flip flop, not the case in vhdl. It just means were connecting 2 wires (signals) together. To get sequential logic have to use a process that's dependent on the clock then change the signal on the rising edge.

Data Types:

bit: Represents a single binary value ('0' or '1').
bit_vector: Represents a vector of binary values. Each element in the vector is of type bit.
std_logic: Represents a single value that can have one of nine possible states ('U', 'X', '0', '1', 'Z', 'W', 'L', 'H', '-'), corresponding to undefined, unknown, logic 0, logic 1, high-impedance, weak signal, weak logic 0, weak logic 1, and don't care, respectively.
std_logic_vector: Represents a vector of std_logic values. Each element in the vector is of type std_logic.
integer: Represents a signed integer value.
natural: Represents an unsigned integer value (non-negative). Can also use positive to exclude 0
real: Represents a floating-point real number.
time: Represents a time value used for simulation purposes.
character: Represents a single ASCII character.
string: Represents a sequence of characters.

Arrays
Single:
type my_array is array (natural range <>) of integer; // Creating the array type
signal my_signal : my_array(0 to 9); // Initializing an array
Double:
type matrix is array (natural range <>, natural range <>) of integer;
signal my_matrix : matrix(0 to 3, 0 to 3);

Signals vs Variables:
Signals are used for interprocess communication and synchronization.
Signals can be read and written from different processes and components.
Signals have a default initial value determined by their data type.
Signal assignments (<=) are scheduled and occur at specific points in time (usually at the end of a simulation cycle).
Changes to a signal within a process become visible to other processes at the end of the current simulation cycle.
Signals are suitable for representing wires, bus lines, and external I/O interfaces in a design.

Variables:
Variables are used for local storage and temporary calculations within a process.
Variables can only be read and written within the same process.
Variables must be explicitly initialized before use.
Variable assignments (:=) are immediate and occur sequentially within a process.
Changes to a variable within a process are immediately visible within the same process.
Variables are suitable for intermediate calculations, loop counters, and temporary storage within processes.

Procedures
procedure procedure_name(parameter1 : parameter_type1; parameter2 :	parameter_type2; ...)
is
    -- Local variable declarations
begin
    -- Procedure body: Statements and logic
end procedure_name;

Functions
function function_name(parameter1 : parameter_type1; parameter2 : parameter_type2; ...) return return_type is
    -- Local variable declarations
begin
    -- Function body: Computation and logic
    return result; -- Return statement with the computed result
end function_name;
Whats the difference between function and procedure? Functions are used to compute and return values, while procedures are used to group statements and perform actions without returning a value. Functions are typically used in expressions, assignments, and computations, while procedures are used for sequencing operations and performing tasks.

Process (like a procedure but it doesn’t get called, it runs when one of its dependencies signals changes)
process_name : process (list_of_dependencies)
begin
….
end process process_name

Assert (Used to throw errors during simulation)
assert data = expected report msg severity error;

msg: is a string variable that you pre-set with the error message.
The assert verifies that data and expected are equal, otherwise it prints the error message during simulation

Packages (create these to use procedures/ functions in other files )
package package_name is
    -- Declarations
end package_name;

package body package_name is
    -- Definitions and implementations
end package_name;

Libraries (Store multiple packages and other things)
library library_name;
use library_name.package_name.all;
A library is a higher-level container that organizes design units, while a package is a construct within a library that contains declarations and provides a mechanism for code reuse and modularity. Libraries provide a way to organize and manage design units, while packages provide a way to group and share common declarations.

Common Library and its packages

IEEE.STD_LOGIC_1164.ALL:
This package defines the standard logic types (STD_LOGIC, STD_LOGIC_VECTOR, etc.) and provides various logical and arithmetic operations for working with these types. It is one of the fundamental packages used in digital design.
std.TextIO.all:
This package provides input/output operations for text-based data. It includes procedures and functions for reading from and writing to text files, as well as formatting and conversion functions.
ieee.std_logic_textio.all:
This package extends the TextIO package and provides additional input/output operations specifically for working with STD_LOGIC types. It includes procedures for reading and writing STD_LOGIC values as characters or strings.
ieee.numeric_std.all:
This package provides a set of numeric types and operations for numerical computations in VHDL. It includes signed and unsigned integer types (signed, unsigned), arithmetic operations, conversion functions, and other utility functions for working with numerical data.
ieee.math_real.all:
This package provides mathematical functions and operations for real numbers. It includes functions for common mathematical operations such as exponentiation, logarithms, trigonometry, and more. These functions operate on real and realtime data types.

Entity & Architecture (entity is like a verilog module with architecture being the definition)
entity MyComponent is
  generic ( // This is optional
    WIDTH : positive := 8
  );
  port (
    input1 : in std_logic_vector(WIDTH-1 downto 0);
    input2 : in std_logic_vector(WIDTH-1 downto 0);
    output : out std_logic_vector(WIDTH-1 downto 0)
  );
end entity MyComponent;

architecture Behavioral of MyComponent is
begin
  -- Architecture implementation here
  -- ...
end architecture Behavioral;

Example:
entity MyEntity is
  generic (
    COUNTER_WIDTH : natural := 8
  );
  port (
    clk : in std_logic;
    reset : in std_logic;
    count : out std_logic_vector(COUNTER_WIDTH - 1 downto 0)
  );
end entity;

architecture Behavioral of MyEntity is
  signal counter : unsigned(COUNTER_WIDTH - 1 downto 0);
begin
  counter_process: process (clk, reset)
  begin
    if reset = '1' then
      counter <= (others => '0');
    elsif rising_edge(clk) then
      counter <= counter + 1;
    end if;
  end process counter_process;

  count <= std_logic_vector(counter);
end architecture;